## Slide 1: Compression Co-Processor

## Slide 2: Overview
Compression Co-processor
communicates with a PC using the RS-232 Serial Port Interface @ 9600 baud
requires 32 Kbytes of RAM for look up tables (LUT)
implemented Lempel-Ziv algorithm (LZ78)

## Slide 3: The LZ78 Compression Algorithm
compresses binary data into a stream of code words.
History-based algorithm in that It does not analyze the incoming data
adds every new string of characters (substrings) within a data stream into a Look-Up-Table (LUT)

## Slide 4: The LZ78 Compression Algorithm
The basic operation of the algorithm revolves around looking through the Look-Up-Table (LUT) for substrings
a substring is a unique string of characters (8bits) that is contained within a data stream

## Slide 5: The LZ78 Compression Algorithm
output code words that can be of any arbitrary length, but it must be expressed in more than a single byte
12-bit code word is implemented
first 256 codes are reserved for the standard ASCII character set with the remaining code words assigned to substrings as the algorithm is executed

## Slide 6: LZ78 Compression Algorithm Example

## Slide 7: Serial Port
In the Idle state logic level ‘1’ is transmitted
A transition from high to low indicates the start of a data word
Start Bit
Stop Bit
Data
“00110001”
Idle
Increasing time

## Slide 8: Serial Port - Hardware Flow Control
CTS/RTS
CTS line is asserted to indicate ready to receive data
  CTS is turned off when output FIFO is full or the ByteEncoder is not ready
  CTS is turned on any other time
Computer always “ready to send” - RTS line not needed
ByteEncoder
4 -byte
lpm_FIFO
RS-232
Out
To
Computer
From
Compression
Engine

## Slide 9: Schematic for External Circuitry

## Slide 10: SRAM
32K X 8 bit word SRAM
100 ns cycle/access time
In our implementation, we achieved a 140ns cycle time and a 160ns access time
VHDL code includes a feature to clear the contents of SRAM

## Slide 11: SRAM Timing Waveforms

## Slide 12: Summary